## Slide 1: Mod 4:Control logic design
Complete processor
Control organization
Design of hardwired control
PLA method
Micro programmed control
Vertical & horizontal microinstructions
Micro program sequencer
Micro programmed cpu organization
..

## Slide 2: COMPLETE PROCESSOR
This has separate processing-units to deal with integer data and floating-point data.
Integer Unit  To process integer data. (Figure 7.14).
Floating Unit  To process floating –point data.
Data-Cache is inserted between these processing-units & main-memory.
The integer and floating unit gets data from data cache.
Instruction-Unit fetches instructions
→ from an instruction-cache or
→ from main-memory when desired instructions are not already in cache.
Processor is connected to system-bus &hence to the rest of the computer by means of a Bus Interface.

## Slide 3: COMPLETE PROCESSOR
• Using separate caches for instructions & data is common practice in many processors today.
• A processor may include several units of each type to increase the potential for concurrent operations.

## Slide 4: CONTROL ORGANIZATION
To execute instructions, the processor must have some means of generating the control-signals.
As for example, during the fetch phase, CPU has to generate PCout signal along with other required signal in the first clock pulse. In the second clock pulse CPU has to generate PCin signal along with other required signals. So, during fetch phase, the proper sequence for generating the signal to retrieve from and store to PC is PCout and PCin.
There are two approaches for this purpose:
1) Hardwired control and 2) Microprogrammed control.

## Slide 5: HARDWIRED CONTROL
Hardwired control is a method of control unit design
The control-signals are generated by using logic circuits such as gates, flip-flops, decoders etc.
Each step in the above sequence is completed in one clock period. A counter may be used to keep track of the control steps.Count of the counter corresponds to one control step

## Slide 6: Hardwired control
The required control signals are determined by
Contents of the control step counter
Contents of the instruction register
Contents of the condition code flags
External input signals(MFC) & interrupt requests.
Decoder/Encoder Block is a combinational-circuit that generates required control-outputs depending on state of all its inputs.

## Slide 7: Separation of decoding & encoding functions

## Slide 8: Hardwired control
Instruction Decoder
 It decodes the instruction loaded in the IR.
 It consists of a separate output-lines INS1 through INSm for each machine instruction.
 According to code in the IR, one of the output-lines INS1 through INSm is set to 1, and all other lines are set to 0.
Step-Decoder provides a separate signal line for each step, or time slot, in the control sequence.

## Slide 9: Hardwired control
Encoder
 It gets the input from instruction decoder, step decoder, external inputs and condition codes.
 It uses all these inputs to generate individual control-signals: Yin, PCout, Add, End and so on.
For example (Figure 7.12), Zin=T1+T6.ADD+T4.BR
This signal is asserted during time-slot T1 for all instructions.
during T6 for an Add instruction.
during T4 for unconditional branch instruction
When RUN=1, counter is incremented by 1 at the end of every clock cycle.
When RUN=0, counter stops counting.(wmfc)
After execution of each instruction, end signal is generated. End signal resets step counter.

## Slide 10: HARDWIRED CONTROL
• Sequence of operations carried out by this machine is determined by wiring of logic circuits, hence the name “hardwired”.
The control hardware can be viewed as a state machine that changes from one state to another in every clock cycle, depending on the contents of the instruction register, condition codes and external inputs.
The outputs of the state machine are the control signals.

## Slide 11: Design methods of hardwired control

## Slide 12: Design procedure of hardwired control
The steps for the design of hardwired control are
1.The problem is stated.
2.An initial equipment configuration is assumed.
3.An algorithm is formulated.
4.The data processor part is specified.
5.The control logic is designed.

## Slide 13: Statement of problem
The problem here is to implement with hardware the addition and subtraction of two fixed point binary numbers represented in sign-magnitude form.
Complement arithematic may be used and the final result must be in sign magntude form.
The addition of 2 number stored in registers of finite length may result in a sum that exceeds the storage capacity of the register by one bit.
The extra bit is said to cause overflow.The circuit must provide a flip flop for storing a possible overflow bit.

## Slide 14: Equipment configuration

## Slide 15: Derivation of algorithm
We designate the magnitude of two numbers by A and B.
When the no:s are added or subtracted, we find that there are eight conditions to consider.
The eight conditions may be expressed in a compact form as follows:
[+/-(A)] +/-[+/-(B)].
If the arithmetic operation specified is subtraction ,we change the sign of B and add,which reduces the no of possible combinations to 4
[+/-(A)] +[+/-(B)].
When the signs of A and B are the same we add two magnitudes and the sign of the result is same as the common sign.When the signs of A and B are not the same,we subtract the smaller number from the larger and the sign of the result is the sign of the larger no.

## Slide 16: Derivation Of algorithm

## Slide 17: Data processor Specification
The operations between A and B can be done with ALU.
The operations with As,Bs and E must be initated with separate control variables.
ALU has 4 selection variables.
The variable L loads the output of the ALU into register A and also the output carry into E.
Variables y,z,w complement Bs,As,and clear E

## Slide 18: Data processor Specification
The control receives five inputs:two from external environment and three from the data processor.To simplfy the design we have S=As xor Bs.
The exclusive or operation is equal to 1,if two signs are not the same,and it is equal to 0 if the signs are both positive or negative.
The control provides an output x for the external circuit.
It selects ALU operations through 4 selection variables S2,S1,S0,Cin.
The other four outputs go to registers in the dataprocessor

## Slide 19: Data processor specification

## Slide 20: Control State Diagram

## Slide 21: Control State diagram

## Slide 22: PLA METHOD Of CONTROL organization

## Slide 23: PLA METHOD

## Slide 24: PLA METHOD

## Slide 25: Micro programmed control: Overview
Control signals are generated by a program similar to machine language programs.
Control Word (CW) is a word whose individual bits represent various control signals.
A sequence of CWs corresponding to the control sequence of a machine instruction constitutes the micro routine;
The individual control words in the micro routine is the microinstruction

## Slide 26: Overview

## Slide 27: ORGANIZATION
The microroutines for all instructions in the instruction-set of a computer are stored in a special memory called the Control Store (CS).
Control-unit generates control-signals for any instruction by sequentially reading CWs of corresponding microroutine from CS.
μPC is used to read CWs sequentially from CS. (μPC Microprogram Counter).
Every time new instruction is loaded into IR, o/p of Starting Address Generator is loaded into μPC.
Then, μPC is automatically incremented by clock;causing successive microinstructions to be read from CS.
Hence, control-signals are delivered to various parts of processor in correct sequence.

## Slide 28: Overview
Control store
One function
cannot be carried
out by this simple
organization.

## Slide 29: Overview
The previous organization cannot handle the situation when the control unit is required to check the status of the condition codes or external inputs to choose between alternative courses of action.
Use conditional branch microinstruction.
Address
Microinstruction
0
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
1
Z
out
,
PC
in
,
Y
in
,
WMF
C
2
MDR
out
,
IR
in
3
Branch
to
starting
address
of
appropriate
microroutine
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
25
If
N=0,
then
branch
to
microinstruction
0
26
Offset-field-of-IR
out
,
SelectY,
Add,
Z
in
27
Z
out
,
PC
in
,
End
Figure 7.17. Microroutine for the instruction Branch<0.

## Slide 30: Modified organization with conditional branching
Figure 7.18. Organization of the control unit to allow
conditional branching in the microprogram.
Control
store
Clock
generator
Starting and
branch address
Condition
codes
inputs
External
CW
IR
m
P
C

## Slide 31: WORKING
The control address register(μPC) holds the address of the next microinstruction to be read.
 When address is available in control address register, the sequencer issues READ command to the control memory.
 After issue of READ command, the word from the addressed location is read into the microinstruction register.
 Now the content of the micro instruction register generates control signals and next address information for the sequencer.
 The sequencer loads a new address into the control address register based on the next address information.

## Slide 32: Working
In case of conditional branching, microinstructions specify which of the external inputs, condition codes should be checked as a condition for branching to take place.
Starting and Branch Address Generator Block loads a new address into μPC when a microinstruction instructs it to do so (Figure 7.18).
To allow implementation of a conditional branch, inputs to this block consist of→ external inputs and condition-codes & → contents of IR.
μPC is incremented every time a new microinstruction is fetched from microprogram memory except in following situations:1) When a new instruction is loaded into IR, μPC is loaded with starting-address of microroutine for that instruction.2) When a Branch microinstruction is encountered and branch condition is satisfied, μPC is loaded with branch-address.3) When an End microinstruction is encountered, μPC is loaded with address of first CW in
microroutine for instruction fetch cycle.

## Slide 33: Microinstructions
A simple way to structure microinstructions is to assign one bit position to each control-signal required in the CPU.
There are 42 signals and hence each microinstruction will have 42 bits.
Drawbacks of microprogrammed control:
1) Assigning individual bits to each control-signal results in long microinstructions because the number of required signals is usually large.
2) Available bit-space is poorly used because only a few bits are set to 1 in any given microinstruction.
Click to add text

## Slide 34: Microinstructions(contd..)
Solution: Signals can be grouped because
1) Most signals are not needed simultaneously.
2) Many signals are mutually exclusive. E.g. only 1 function of ALU can be activated at a time.
For ex: Gating signals: IN and OUT signals (Figure 7.19).
Control-signals: Read, Write. ALU signals: Add, Sub, Mul, Div;
3)A source for data transfers must be unique which means that it should not be possible to get the contents of two different registers on to the bus at the same time.
4)Read and Write signals to the memory cannot be activated simultaneously.
Grouping control-signals into fields requires a little more hardware because decoding-circuits must be used to decode bit patterns of each field into individual control-signals.
• Advantage: This method results in a smaller control-store (only 20 bits are needed to store the patterns for the 42 signals).

## Slide 36: Vertical & horizontal organization
TECHNIQUES OF GROUPING OF CONTROL-SIGNALS
The grouping of control-signal can be done either by using
Vertical organization & 2) Horizontal organization.
Vertical organization
Highly encoded scheme that can be compact codes to specify only a small number of control functions in each microinstruction are referred to as a vertical organization.
Horizontal organization
The minimally encoded scheme, in which resources can be controlled with a single instruction is called a horizontal organization.

## Slide 37: Difference between vertical & horizontal organization

## Slide 38: Difference between hardwired & microprogrammed control

## Slide 39: Microinstructions
The microinstructions are broadly classified into
1)Vertical microinstructions
2)Horizontal microinstructions
Horizontal microinstructions: In the horizontal microinstruction, each bit of the microinstruction represents a microorder or control signal, which directly controls a single bus line or sometimes a gate in the machine. The length of the such microinstruction may be hundreds of bits.

## Slide 40: Vertical microinstructions
In vertical microinstructions, many similar control signals can be encoded into few microinstruction bits. For eg, for 16 ALU operations, which may require 16 individual microorders in horizontal microinstruction, only 4 encoded bits are needed in vertical microinstructions.
These encoded bits need to be passed from respective decoders to get individual control signals

## Slide 41: Control of processor unit
The hardware organization of a microprogram control unit must have general purpose configuration to suit a wide variety of situations.
A general purpose microprogram control unit must have control memory, control variables and multiplexer and select bits to check status bits.
Advantage of microprogram control: once hardware configuration is established, no further need to change the hardware
To establish a different control sequence ,all we need to do is specify is the different set of microinstructions for the control memory(ie, change the microprogram)

## Slide 42: Control of processor unit
In the control of the processor unit, we have a processor unit(7 registers, ALU, shifter, status register)
A microoperation is selected with a control word of 16 bits.
It has a control memory of 64 words with 26 bits per word.
To select 64 words = need 6 bits of address.
To select 8 status bits=need 3 selection lines for multiplexer.
1 bit of micro instruction selects between an external address and address field of microinstruction.
Adding 16 bits for selecting microoperation in the processor a total of 26 bits for each microinstruction

## Slide 43: Control of processor unit(contd…)
The first 16 bits of microinstruction select the microopeartion for the processor.
The other 10 bits select the next address for the control address register.
The status bits from the processor are applied to the inputs of the multiplexer.
Both the normal and complement values are used,except for the overflow bit V.
Input 0 of mux2 is connected to binary constant which is always 1.
The load input to CAR is enabled when input 0 of mux is selected by 18,19,20 in the micro instruction.This causes a transfer of information from output mux1 into CAR

## Slide 44: Control of processor unit(contd…)
The input into CAR is a function of bit 17 in the microinstruction.
If bit 17=1;then CAR receives the address field if microinstruction. If bit 17=0,then external address loaded into CAR. The external address is for the purpose of initiating a new sequence of microinstructions
The status bit or complement is selected by 18,19,20 of the microinstruction may be equal to 1 or 0.The input address is loaded into CAR if the selected bit =1,but CAR is incremented if the selected bit is 0
The sign n zero bits are affected by all operations. The carry and overflow bits donot change after the four logic operations and the increment and decrement operation

## Slide 46: Microprogrammed computer Organization

## Slide 47: MICRO PROGRAMMED COMPUTER ORGANIZATION
A digital computer consists of a central processor unit (CPU) ,a memory unit, and input - output devices
The CPU can be classified into two distinct but interactive functional sections.
One section is the processing section and other is the control section
A block diagram of micro programmed computer shown above figure

## Slide 48: MICRO PROGRAMMED COMPUTER ORGANIZATION
It consist of
Memory unit
Two processor unit
A micro program sequencer
A control memory
And few other digital functions

## Slide 49: MICRO PROGRAMMED COMPUTER ORGANIZATION
The memory unit stores the instruction and data supplied by the user through an input
device
The data processor manipulates the data
The address processor manipulates the address information received from memory
An instruction extracted from memory during fetch cycle goes into the instruction register

## Slide 50: MICRO PROGRAMMED COMPUTER ORGANIZATION
The micro program control unit consist of the sequencer of
A control memory for storing microinstructions, a multiplexer and a pipeline register
A multiplexer select one of many status and applied it to the T (test) input of sequencer
The pipeline register is not always necessary because output from control memory can
go directly to the control input of various unit in the CPU
However a pipelineKregTisterUspeeded up the control operation
It allow next address to be generated and output of control memory to change while the current control word in the pipeline register will initiate the micro operations given by the present micro operations

## Slide 51: MICRO PROGRAMMED COMPUTER ORGANIZATION
The possible micro instruction format for the control memory is illustrated within the pipeline
register
The I filed consist of 3 bit and supplies the input information for the sequencer
The SL field select a status bit for the multiplexer
The BRANCH field is the address filed of micro instruction and supplies a branch address to the
sequencer
These three field of micro operation provide information to the sequencer generate the next address and
the control memory reads the next micro instructions are being executed in the other unit of
CPU
K TU STUDNTS

## Slide 52: MICRO PROGRAMMED COMPUTER ORGANIZATION
The other three filled in the microinstruction are for controlling the micro operations in the
processor and memory units
The memory control(MC) field controls the address processor and the read and write operations in the memory unit
The last field is a dKata fTield U(DF) useSd to iTntroUduceDthe NconsTtantSinto the processor.
The processor field (PS) control the operations in the data processor unit.

## Slide 53: Microprogrammed computer organization(contd..)
An instruction extracted from memory during fetch cycle goes into the instruction register.
The instruction code bits in the IR specify macrooperation for control memory.
Code transformation converts the operational code bits of an instruction to starting address for the control memory.
Code transformation consists of a mapping function,the address generated by the mapping function is applied to EXA input of the sequnencer.

## Slide 54: Introduction: Microprogram sequencer
The basic components of a micro-programmed control unit are the control memory and the circuits that select the next address. The address selection part is called microprogram sequencer.
The purpose of a microprogram sequencer is to present an address to the control memory so that the microinstruction may be read and executed.
The next address logic of the sequencer determines the specific address source to be loaded into the control address register.
The choice of the address source is guided by the next address information bits that the sequencer receives from present micro instruction.

## Slide 55: Microinstruction code format

## Slide 56: Design of microprogram sequencer
The task of microprogram sequencing is done by microprogram sequencer.
2 important factors must be considered while designing the microprogram sequencer:
a) The size of the microinstruction b) The address generation time.
The size of the microinstruction should be minimum so that the size of control memory required to store microinstructions is also less. This reduces the cost of control memory.
With less address generation time, microinstruction can be executed in less time resulting better throughout.

## Slide 57: Design of microprogram sequencer
A microprogram sequencer inspects certain bits of the microinstruction,from which it determines the next address for the control memory.
A typical sequencer provides the following address sequencing capabilities:
1.Increments the present address for control memory
2.Branches to an address as specified by the address field of microinstruction
3.Branches to a given address if specified status bit is equal to 1.
4.Transfers control to a new address as specified by an external source.
5.Has a facility for subroutine calls and returns.

## Slide 58: Design of microprogram sequencer
In most cases the microinstructions are read from the control memory in succession, which is accomplished by incrementing the address register for control memory.
In some cases, each microinstruction contains an address field even for sequential addresses, which eliminates the need to increment the CAR, coz the address field in each microinstruction specifies the address of next microinstruction.
Provision must be available for branching to an address out of normal sequence.
Control must be transferred to non sequential microinstruction,thus the sequencer must provide the capability for branching to any one of 2 address,depending on whether status bit is 0 or 1.
Branch to the address specified by the address field of microinstruction if status bit=1 and to next address in sequence if status bit=0

## Slide 59
Multiplexer that selects an address from 4 sources and routes it into CAR.
The output from CAR provides the address for control memory.
The contents of CAR are incremented and applied to multiplexer and to stack register file.
Inputs I0,I1,I2 specify the operation for the sequencer and input T is a test point for status bit.
The address register can be cleared to 0 to initialize the system and clock pulses synchronize the loading into the registers.

## Slide 62: Push and pop stack operations