## Slide 1: Module: 2
Syllabus: Register transfer logic: inter register transfer – arithmetic, logic and shift micro operations. Processor logic design: - processor organization – Arithmetic logic unit - design of arithmetic circuit - design of logic circuit - Design of arithmetic logic unit - status register – design of shifter - processor unit – design of accumulator.
CST 202
Computer Organization and Architecture

## Slide 2: Module: 2
Part 1 :
REGISTER TRANSFER LOGIC
CST 202
Computer Organization and Architecture

## Slide 3: Introduction
The information flow and the processing task among the data stored in the registers can be described by means of register transfer logic
Components of Register Transfer Logic
The set of registers in the system and their functions: eg; shift registers, counters and memory units.
The binary-coded information stored in the registers: eg; binary numbers, binary coded decimal numbers, alphanumeric characters, control information or any other binary coded information.
The operations performed on the information stored in the registers: --micro operations. Examples are shift, count, add, clear and load
The control functions that initiate the sequence of operations: timing signals that sequence the operations one at a time.

## Slide 4
Register transfer language(Computer hardware description language)
Symbolic notation used for registers, for specifying operations on the contents of registers and specifying control functions .
A statement in a register transfer language consists of control function and a list of micro-operations
Micro-Operation:
Operations performed in data stored in registers.
Elementary operation that can be performed parallel during one clock pulse period.
The result of operation may replace the previous binary information of a register or may be transferred to another register.
Example: Shift, count, clear, add & load
A micro-operation requires one clock pulse for the execution if the operation done in parallel. In serial computer a micro-operation requires a number of clock pulses equal to the word time in the system

## Slide 5
Types of Binary Information
Numerical data such as binary numbers or binary-coded decimal numbers.
Non-numerical data such as alphanumeric characters or other binary-coded symbols.
Instruction codes, addresses and other control information used to specify the data processing requirements in the system

## Slide 6
Types of Micro-Operations in digital system
Interregister transfer micro-operation: Do not change the information content when the binary information moves from one register to another
Arithmetic operation: Perform arithmetic on numbers stored in registers.
Logic microoperation: Perform operations such as AND and OR on individual pairs of bits stored in registers.
Shift microoperation: Specify operations for shift registers.

## Slide 7: INTER REGISTER TRANSFER
Computer registers are designated by capital letters (sometimes followed by numerals) to denote the function of the register.
R1 - Processor Register,
MAR - Memory Address Register (holds an address for a memory unit)
PC - Program Counter
IR - Instruction Register
SR: Status Register
The cells or flipflops of n-bit register are numbered in sequence from1 to n (from 0 to n-1) starting either from left or from right

## Slide 8: INTER REGISTER TRANSFER (CONTD.)
The register can be represented in 4 ways:
Rectangular box with name of the register inside,
The individual cells is assigned a letter with a subscript number,
The numbering of cells from right to left can be marked on top of the box,
16 bit register is partitioned into 2 parts , bits 1 to 8 are assigned the letter L(for low) and bits 9 to 16 are assigned the letter H(for high)

## Slide 9: Block diagram of Register
Registers can be specified in a register transfer language with a declaration statement.
For example: Registers in the above figure can be defined with declaration statement such as
DECLARE REGISTER A(8), MBR(12), PC(16)
DECLARE SUBREGISTER PC(L) = PC(1-8), PC(H) = PC(9-16).

## Slide 10
Information transfer from one register to another is described by a replacement operator: A ← B.
This statement denotes a transfer of the content of register B into register A and this transfer happens in one clock cycle.
After the operation, the content of the B (source) does not change.
The content of the A (destination) will be lost and replaced by the new data transferred from B.

## Slide 11
Hardware implementation of a controlled transfer:
x’T1: A ← B is as follows :-
Conditional transfer occurs only under a control condition: Representation of a (conditional) transfer x’T1: A ← B.
A binary condition (x’T1 equals to 0 or 1) determines when the transfer occurs.
In this the content of B is transferred into A only if x is 0 and T1 is 1.

## Slide 12
Destination register receives information from two sources but not at the same time
T1 : C ← A
T2 : C ← B
The connection of two source register to the same destination register cannot be done directly, but requires a multiplexer circuit to select between two possible paths.

## Slide 13
Basic symbols of Register Transfer Logic

## Slide 14: Bus transfer
Paths must be provided to transfer information from one register to another in a digital computer
Efficient scheme is common bus system.
Bus structure -a set of common lines, one for each bit of a register, through which binary information is transferred one at a time.
Control signals determine which register is selected by the bus during each particular register transfer.
Done using multiplexers.
The multiplexers select the source register whose binary information is then placed on the bus.
Click to add text

## Slide 15
Here, bits in the same significant position in each register are connected to the data inputs of one multiplexer to form one line of the bus.
MUX 0 multiplexes the four 0 bits of the registers,
MUX 1 multiplexes the four 1 bits of the registers, and similarly for the other two bits.

## Slide 16: Memory Transfer
1. Read operation : Transfer of information from a memory word to the outside environment
Read: MDR←M
(transfer from the selected memory register M into MDR (memory data register))
2. Write operation: Transfer of new information to be stored into the memory
Write: M ← MDR
(transfer from MDR to the selected memory register M)
Note:
M-> a memory word

## Slide 17
Consider a memory unit that receives the address from a register, called the address register, symbolized by AR.
The data are transferred to another register, called the data register, symbolized by DR.
The memory read operation can be stated as follows:
Read: DR ← M [AR]
This causes a transfer of information into DR from the memory word M selected by the address in AR.
The memory write operation transfers the content of a register R1 to a memory word M selected by the address in address AR.
The notation is:
Write: M [AR] ← R1

## Slide 18
Fig: memory unit that communicate with multiple registers

## Slide 19: ARITHMETIC, LOGIC AND SHIFT MICRO OPERATION
Arithmetic Micro-Operation
Basic arithmetic micro-operations are:
Addition
Subtraction,
Increment,
Decrement
Arithmetic shift.
(3) And (4)-> done using combinational circuit or a binary up-down counter because of plus-one and minus-one operation respectively.

## Slide 20
Arithmetic add microoperations are defined by the statement
F ← A + B
Explanation:
Contents of register A are to be added to the contents of register B and the sum is transferred to register F
3 registers A, B and F and a digital function that performs the addition operation such as parallel adder needed.

## Slide 21
Consider the statements
T2 : A ← A + B
T5 : A ← A + 1
T2 -add the contents of register B to the present contents of A with a parallel adder.
T5 -increments register A with a counter.
The transfer of the sum from parallel adder into register A can be activated with a load input in the register.
Register be a counter with parallel load capability.
The parallel adder receives input information from registers A and B.
The sum bits from the parallel adder are applied to the inputs of A and timing variable T2 loads the sum into register A.
Timing variable T5 increments there by enabling increment input register

## Slide 22
2. Logic Micro-Operations
Binary operations for strings of bits stored in registers
Eg: F ← A ⊕ B (exclusive-OR micro-operation )
Let A =1010 and B=1100
Therefore, F= 0110
Less used but very useful for bit manipulation of binary data and for making logical decisions.

## Slide 23
Logic and Shift Micro instructions are:-
Example:
T1 + T2 : A ← A + B, C ← D ∨ F
First + means OR operation between 2 timing variables of a control function
Second + means add microoperation

## Slide 24
3. Shift Micro-Operations[study examples from notebook]
Shift the contents of a register either left or right
used for serial transfer of data
used along with arithmetic, logic, and other data-processing operations.
shl - shift left
shr - shift right
Example: A ← shl A 1-bit shift to the left of register A
B ← shr B 1-bit shift to the right of register B
3 types of shifts: logical, circular, and arithmetic.
Example:
A ← shl, A1 ← An i.e, Circular shift that tranfers the leftmost bit from An into the rightmost flipflop A1.
A ← shr, An ← E i.e, Shift right operation with the leftmost flip flop An receiving the value of the 1-bit register E

## Slide 25
Part 2
PROCESSOR LOGIC DESIGN

## Slide 26: PROCESSOR ORGANIZATION
Processor part -data path of the CPU (Because processor forms the paths for the data transfers between the registers in the unit
Data paths by buses and other common lines
Control gates that formulate the given path are - multiplexers and decoders whose selection lines specify the required path.

## Slide 27: Bus Organization(4 processor registers)

## Slide 28
Register connected to two MUX to form input buses A and B.
The selection lines of each MUX select one register for the particular bus.
The A and B buses are applied to a common ALU.
The function selected in the ALU determines the particular operation that is to be performed.
The shift micro-operations are implemented in the shifter.
The result of the micro-operation goes through the output bus S into the inputs of all registers.
The destination register that receives the information from the output bus is selected by a decoder.
When enabled, this decoder activates one of the register load inputs to provide a transfer path between the data on the S bus and the inputs of the selected destination register.
The output bus S provides the terminals for transferring data to an external destination.
One input of MUX A or B can receive data from the outside
The control unit that supervises the processor bus system directs the information flow through the ALU by selecting the various components in the unit.

## Slide 29: Example
To perform the microoperation:
R1←R2+ R3
The control must provide binary selection variables to the following selector inputs:
1. MUX A selector: to place the contents of R2 onto bus A.
2. MUX B selector: to place the contents of R3 onto bus B.
3. ALU function selector: to provide the arithmetic operation A + B.
4. Shift selector: for direct transfer from the output of the ALU onto output bus S (no shift).
5. Decoder destination selector: to transfer the contents of bus S into R 1.

## Slide 30
Accumulator Register - for short-term, intermediate storage of arithmetic and logic data in a computer's CPU
To find the Sum of two numbers stored in processor registers:
T1: A ← 0 Clear A
T2: A ← A + R1 Transfer R1 to A
T3: A ← A + R2 Add R2 to A

## Slide 31
Status Registers – to store condition-code bits/ flag bits/status bit
The relative magnitude of two numbers may be
determined by subtracting one number from the other and
then checking certain bit conditions in the resultant difference
4 bit register- C (carry), Z (zero),S (sign) and V (overflow)
These bits are set or cleared as a result of an operation performed in the ALU
• Bit C is set if the output carry of an ALU is 1.
• Bit S is set to 1 if the highest order bit of the result in the output of the ALU is 1.
• Bit Z is set to 1 if the output of the ALU contains all O's.
• Bit V is set if the exclusive —OR of carries C8 and C9 is 1, and cleared otherwise. This is the condition for overflow when the numbers are in signed 2's complement representation. For an 8 bit ALU, V is set if the result is greater than 127 or less than -128.

## Slide 32
Status Registers

## Slide 33
Example
If Z=1,we knows that A=B, since A-B=0. If Z=0, then we know that A is not equal to B.
C=1 if A>=B and C=0 if A<B.

## Slide 34: ARITHMETIC LOGIC UNIT (ALU)
Fig:4-bit ALU
ALU- multi operation, combinational-logic digital function.
Perform a set of basic arithmetic and logic operations.
Selection lines to select a particular operation in the unit.
k selection variables can specify up to 2k distinct operations

## Slide 35
Design of Arithmetic Circuit
Basic component- parallel adder(full adders cascaded)
Input carry Cin goes to the full-adder circuit in the least significant bit position.
Output carry Cout comes from the full-adder circuit in the most significant bit position.
Input B is applied in four different form by using following circuit
The input A is applied directly to the 4-bit parallel adder and the input B is modified. The resultant arithmetic circuit is shown next.

## Slide 37
Function table for the arithmetic circuit

## Slide 38
Design of Logic Circuit
16 logic operations can be generated in one circuit and selected by means of four selection lines.
Can be obtained by means of AND, OR, and NOT (complement) operations
For three operations, we need two selection variables
But two selection lines can select among four logic operations, so we choose also the exclusive-OR (XOR) function for the logic circuit to be designed
The diagram(next slide) shows one typical stage designated by subscript i. The circuit must be repeated n times for an n-bit logic circuit

## Slide 39
Fig: Logic diagram
Fig: Function Table

## Slide 40
Design of Arithmetic Logic Unit
Logic circuit + Arithmetic circuit =Arithmetic Logic Unit.
S1 and S0 can be made common to both sections
A third selection variable, S2, is used to differentiate between the two
The outputs of the logic and arithmetic circuits in each stage go through a multiplexer with selection variable S2.
When S2 = 0, the arithmetic output is selected,
when S2 = 1, the logic output is selected

## Slide 41
More efficient method:- by inhibiting all input carries into the full-adder circuits of the parallel adder.
Consider the Boolean function that generates the output sum in a full-adder circuit:
F=X ⊕ Y ⊕ Cin
The input carry Cin in each stage can be made to be equal to 0 when a selection variable S2 is equal to 1.
The result would be:
F=X ⊕ Y
This expression is valid because of the property of the X-OR operation:
X⊕0 = X

## Slide 42
Design steps
1. Design the arithmetic section independent of the logic section.
2. Determine the logic operations obtained from the arithmetic circuit in step 1, assuming that the input carries to all stages are 0.
3. Modify the arithmetic circuit to obtain the required logic operations.

## Slide 43
Cin
S2
S1
S0
A1
B1
A2
B2
C1
C2
F1
F2
X1
Y1
X2
Y2
FA
FA
C3
Cout
Fig: Final ALU

## Slide 44
The inputs to each full-adder circuit are specified by the Boolean functions:
Xi = Ai + S2 S1’ S0’Bi + S2 S1 S0’ Bi
Yi = S0 Bi + S1 Bi’
Zi = S2’ Ci
When S2 = 0, the three functions reduce to:
Xi = Ai
Yi = S0 Bi + S1 Bi’
Zi = Ci , which are the function for the arithmetic circuit.
The logical operations are generated when S2 = 1.
For S2 S1 S0 = 1 0 1 or 1 1 1, the function reduce to:
Xi = Ai Yi = S0 Bi + S1 Bi’ Zi = 0

## Slide 45
Function table for the Arithmetic and Logic Unit

## Slide 46
Design of Combinational Logic Shifter
The shift unit attached to the processor transfers the output of the ALU onto the output bus.
Shifter may function in four different ways.
1. The shifter may transfer the information directly without a shift.
2. The shifter may shift the information to the right.
3. The shifter may shift the information to the left.
4. In some cases no transfer is made from ALU to the output bus.

## Slide 47
A shifter is a bi-directional shift-register with parallel load.
The information from ALU can be transferred to the register in parallel and then shifted to the right or left.
In this configuration, a clock pulse is needed for the transfer to the shift register, and another pulse is needed for the shift.
Another clock pulse may also in need of when information is passed from shift register to destination register.
The number of clock pulses may reduce if the shifter is implemented with a combinational circuit.
A combinational—logic shifter can be constructed with multiplexers

## Slide 48
Fig: 4-bit combinational-logic shifter
Shifter operation can be selected by two variables H1 H0
• If H1 H0 = 0 0 No shift is executed and the signal from F go directly to S lines
• If H1 H0 = 0 1 Shift Right is executed
• If H1 H0 = 1 0 Shift Left is executed
• If H1 H0 = 1 1 No operations

## Slide 49
PROCESSOR UNIT
Fig: Block Diagram

## Slide 50
Explanation:
It consists of seven registers R1 through R7 and a status register.
The outputs of the seven registers go through two multiplexers to select the inputs to the ALU.
Fig: Control Word
  Input data from an external source are also selected by the same
  multiplexers.
  The output of the ALU goes through a shifter and then to a set of
  external output terminals

## Slide 51
Functions of all selection variables

## Slide 52
The 3-bit binary code listed in the table specifies the code for each of the five fields A, B, D, input data, F, and H.
The register selected by A, B, and D is the one whose decimal number is equivalent to the binary number in the code.
When the A or B field is 000, the corresponding multiplexer selects the input data.
When D = 000, no destination register is selected.
The three bits in the F field, together with the input carry Cin, provide the 12 operations of the ALU
There are two possibilities for F = A.
Carry bit C is cleared,
Carry bit C is set to 1.

## Slide 53
DESIGN OF ACCUMULATOR
Fig: Block diagram of Accumulator

## Slide 54
A register + associated combinational circuit =sequential circuit.
A register= Accumulator register (AC)
Accumulator refers to both the A register and its associated combinational circuit.
The external inputs to the accumulator are the data inputs from B and the control variables that determine the micro operations for the register.
The next state of register A is a function of its present state and of the external inputs.
Accumulator can also perform data processing operations.

## Slide 55
Total of nine operations is considered here for the design of accumulator circuit.
A=source register.
B =second source register.
estination register is also accumulator register itself. For a complete accumulator there will be n stages.

## Slide 56
Total of nine operations is considered here for the design of accumulator circuit.
A=source register.
B =second source register.
Destination register =accumulator register
For a complete accumulator there will be n stages.

## Slide 57
Fig: 4-bit Accumulator constructed with 4 stages

## Slide 58
Explanation of design
The inputs and outputs of each stage can be connected in cascade to form a complete accumulator.
The number on top of each block represents the bit position.
All blocks receive 8 control variables P1 to P8 and the clock pulses from CP.
The other six inputs and four outputs are same as with the typical stage.
The zero detect chain is obtained by connecting the z variables in cascade, with the first block receiving a binary constant I .
The last stage produces the zero detect variable Z.
Total number of terminals in the 4 bit accumulator is 25, including terminals for the A outputs.
Incorporating two more terminals for power supply, the circuit can be enclosed within one IC package having 27 or 28 pins.
The number of terminals for the control variable can be reduced from 9 to 4 if a decoder is inserted in the IC.
In such cases, IC pin count is also reduced to 22 and the accumulator can be extended to 16 microoperations without adding external pins (That is, with 4 bits we can identify 16 operations).