## Slide 1: Pipelining Hazards

## Slide 2: Types of Pipeline hazards
Structural hazards: Hardware cannot support certain combinations of instructions (two instructions in the pipeline require the same resource).
Data hazards: Instruction depends on result of prior instruction still in the pipeline
Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps).

## Slide 3
Structural hazards arise because there is not enough duplication of resources.
Resolving structural hazards:
Solution 1: Wait o Must detect the hazard Must have mechanism to stall
Solution 2: Throw more hardware at the problem
o Pipeline hardware resource
o Replicate resource

## Slide 4: Data Hazards
Data hazards may be classified as one of three types, depending on the order of read and write accesses in the instructions:
RAW (Read After Write)
Corresponds to a true data dependence
Program order must be preserved
This hazard results from an actual need for communication
Considering two instructions i and j, instruction j reads the data before i writes it
i: ADD R1, R2, R3
j: SUB R4, R1, R3
Add modifies R1 and then Sub should read it. If this order is changed, there is a RAW hazard

## Slide 5: Data forwarding to avoid RAW
In order to avoid RAW hazards, IBM engineers developed a short circuiting approach which gives a copy of the data object to be written directly to the instruction waiting to read the data. This concept was generalized into a technique known as data forwarding, which forward multiple copies of the data to as many waiting instructions as may wish to read it. A data forwarding chain can be established in some cases. The internal forwarding and register-tagging techniques are helpful in resolving logic hazards in pipelines.

## Slide 6: WAW (Write After Write)
Corresponds to an output dependence
Occurs when there are multiple writes or a short integer pipeline and a longer floating-point pipeline or when an instruction proceeds when a previous instruction is stalled WAW (write after write)
This is caused by a name dependence. There is no actual data transfer. It is the same name that causes the problem
Considering two instructions i and j, instruction j should write after instruction i has written the data
i: SUB R1, R4, R3
j: ADD R1, R2, R3
Instruction i has to modify register r1 first, and then j has to modify it. Otherwise, there is a WAW hazard. There is a problem because of R1. If some other register had been used, there will not be a problem
Solution is register renaming, that is, use some other register. The hardware can do the renaming or the compiler can do the renaming

## Slide 7: WAR (Write After Read)
Arises from an anti dependence
Occurs either when there are early writes and late reads, or when instructions are re-ordered
There is no actual data transfer. It is the same name that causes the problem
Considering two instructions i and j, instruction j should write after instruction i has read the data.
i: SUB R4, R1, R3
j: ADD R1, R2, R3
Instruction i has to read register r1 first, and then j has to modify it. Otherwise, there is a WAR hazard. There is a problem because of R1. If some other register had been used, there will not be a problem
• Solution is register renaming, that is, use some other register. The hardware can do the renaming or the compiler can do the renaming