## Slide 1: Mod 5Part 1:I/O Organization
Accessing of I/O devices
Interrupts
Direct memory access

## Slide 2: Accessing I/O devices/Interfacing I/O
Bus
I/O de
vice 1
I/O de
vice
n
Processor
Memory
Multiple I/O devices may be connected to the processor and the memory via a bus.
Bus consists of three sets of lines to carry address, data and control signals.
Each I/O device is assigned an unique address.
To access an I/O device, the processor places the address on the address lines.
The device recognizes the address, and responds to the control signals(read/write).

## Slide 3: Accessing I/O devices (contd..)
      Based on Address Space used by I/O devices:
I/O devices and the memory may share the same address space:Memory mapped i/o
  Memory-mapped I/O.
  Any machine instruction that can access memory can be used to transfer data to or from an I/O device.
  Simpler software. Motorola
      I/O devices and the memory may have different address spaces: Isolated I/O or I/O Mapped I/O
  Special instructions to transfer data to and from I/O devices.
  I/O devices may have to deal with fewer address lines.
  I/O address lines need not be physically separate from memory address lines.
  In fact, address lines may be shared between I/O devices and memory, with a control signal to indicate whether it is a memory address or an I/O address.
  Intel, Zilog

## Slide 4: Accessing I/O devices (contd..)
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input device
Bus
Address lines
Data lines
Control lines
I/O device is connected to the bus using an I/O interface circuit which has:
- Address decoder, control circuit, and data and status registers.
Address decoder decodes the address placed on the address lines thus enabling the
device to recognize its address.
Data register holds the data being transferred to or from the processor.
Status register holds information necessary for the operation of the I/O device.
Data and status registers are connected to the data lines, and have unique addresses.
I/O interface circuit coordinates I/O transfers.

## Slide 5: Accessing I/O devices (contd..)
Recall that the rate of transfer to and from I/O devices is slower than the speed of the processor. This creates the need for mechanisms to synchronize data transfers between them.
Program-controlled I/O:
  Processor repeatedly monitors a status flag to achieve the necessary synchronization.
  Processor polls the I/O device.
  use dedicated I/O instructions in the processor
CPU has direct control over I/O
– Sensing status
– Read/write commands
– Transferring data
CPU waits for I/O module to complete operation
Wastes CPU time
Two other mechanisms used for synchronizing data transfers/(MODES OF DATA TRANSFER) between the processor and memory:
  Interrupts.
  Direct Memory Access.

## Slide 6: Interrupts
In program-controlled I/O, when the processor continuously monitors the status of the device, it does not perform any useful tasks.
An alternate approach would be for the I/O device to alert the processor when it becomes ready.
  Do so by sending a hardware signal called an interrupt to the processor.
  At least one of the bus control lines, called an interrupt-request line is dedicated for this purpose.
Processor can perform other useful tasks while it is waiting for the device to be ready.

## Slide 7: Interrupts (contd..)
Interrupt Service routine
Program 1
here
Interrupt
occurs
M
i
2
1
i
1
+
Processor is executing the instruction located at address i when an interrupt occurs.
Routine executed in response to an interrupt request is called the interrupt-service routine.
When an interrupt occurs, control must be transferred to the interrupt service routine.
But before transferring control, the current contents of the PC (i+1), must be saved in a known
location.
This will enable the return-from-interrupt instruction to resume execution at i+1.
Return address, or the contents of the PC are usually stored on the processor stack.

## Slide 8: Interrupts (contd..)
Treatment of an interrupt-service routine is very similar to that of a subroutine.
However there are significant differences:
  A subroutine performs a task that is required by the calling program.
  Interrupt-service routine may not have anything in common with the program it interrupts.
  Interrupt-service routine and the program that it interrupts may belong to different users.
  As a result, before branching to the interrupt-service routine, not only the PC, but other information such as condition code flags, and processor registers used by both the interrupted program and the interrupt service routine must be stored.
  This will enable the interrupted program to resume execution upon return from interrupt service routine.

## Slide 9: Interrupts (contd..)
Saving and restoring information can be done automatically by the processor or explicitly by program instructions.
Saving and restoring registers involves memory transfers:
  Increases the total execution time.
  Increases the delay between the time an interrupt request is received, and the start of execution of the interrupt-service routine. This delay is called interrupt latency.
In order to reduce the interrupt latency, most processors save only the minimal amount of information:
  This minimal amount of information includes Program Counter and processor status registers.
Any additional information that must be saved, must be saved explicitly by the program instructions at the beginning of the interrupt service routine.

## Slide 10: Interrupts (contd..)
When a processor receives an interrupt-request, it must branch to the interrupt service routine.
It must also inform the device that it has recognized the interrupt request.
This can be accomplished in two ways:
  Some processors have an explicit interrupt-acknowledge control signal for this purpose.
  In other cases, the data transfer that takes place between the device and the processor can be used to inform the device.

## Slide 11: Interrupts (contd..)
Interrupt-requests interrupt the execution of a program, and may alter the intended sequence of events:
  Sometimes such alterations may be undesirable, and must not be allowed.
  For example, the processor may not want to be interrupted by the same device while executing its interrupt-service routine.
Processors generally provide the ability to enable and disable such interruptions as desired.
One simple way is to provide machine instructions such as Interrupt-enable and Interrupt-disable for this purpose.
To avoid interruption by the same device during the execution of an interrupt service routine:
  First instruction of an interrupt service routine can be Interrupt-disable.
  Last instruction of an interrupt service routine can be Interrupt-enable.

## Slide 12: Enabling & Disabling Interrupt
Device activates interrupt signal line and waits with this
signal activated until processors attends
The interrupt signal line is active during execution of ISR
and till the device caused interrupt is serviced
Necessary to ensure that the active signal does not lead to
successive interruptions (level-triggered input) causing the system to fall in infinite loop.
• What if the same device interrupts again, within an ISR ?
• Three methods of Controlling Interrupts (single device)
– Ignoring interrupt
– Disabling interrupts
– Special Interrupt request line

## Slide 13
Ignoring Interrupts
– Processor hardware ignores the interrupt request line
until the execution of the first instruction of the ISR
completed
– Using an interrupt disable instruction after the first
instruction of the ISR – no further interrupts
– A return from interrupt instruction is completed before
further interruptions can occur
Disabling Interrupts
– Processor automatically disables interrupts before starting the execution of the ISR
– The processor saves the contents of PC and PS (status register) before performing interrupt disabling.
– The interrupt-enable is set to 0 – no further interrupts allowed
– When return from interrupt instruction is executed the
contents of the PS are restored from the stack, and the
interrupt enable is set to 1

## Slide 14: Enabling and Disabling Interrupts
Special Interrupt line
– Special interrupt request line for which the interrupt
handling circuit responds only to the leading edge of
the signal
– Edge –triggered
– Processor receives only one request regardless of
how long the line is activated
– No separate interrupt disabling instructions

## Slide 15: The sequence of events involved in handling an interrupt request from a single device.
Assuming that interrupts are enabled, following is a typical scenario
The device raises an interrupt request
The processor interrupts the program currently executed
Interrupts are disabled by changing the control bits in the PS(Except in the case of edge triggered interrupts)
The device is informed that its request has been recognized and in response it deactivates the interrupt request signal.
The action requested by the interrupt is performed by the isr.
Interrupts are enabled and execution of the interrupted program is resumed

## Slide 16: Interrupts: Handling Multiple Devices
Multiple I/O devices may be connected to the processor and the memory via a bus. Some or all of these devices may be capable of generating interrupt requests.
  Each device operates independently, and hence no definite order can be imposed on how the devices generate interrupt requests?
How does the processor know which device has generated an interrupt?
How does the processor know which interrupt service routine needs to be executed?
When the processor is executing an interrupt service routine for one device, can other device interrupt the processor?
If two interrupt-requests are received simultaneously, then how to break the tie?

## Slide 17: Handling Multiple Devices
Multiple devices can initiate interrupts
• They uses the common interrupt request line
• Techniques are
– Polling
– Vectored Interrupts
– Interrupt Nesting
– Daisy Chaining

## Slide 18: Polling Scheme
Consider a simple arrangement where all devices send their interrupt-requests over a single control line in the bus.
When the processor receives an interrupt request over this control line, how does it know which device is requesting an interrupt?
Polling Scheme(The simplest way to identify the interrupting device is to have the ISR routine poll all I/O Devices connected to bus)
•The IRQ (interrupt request) bit in the status register is
set when a device is requesting an interrupt.
• The Interrupt service routine polls the I/O devices
connected to the bus.
• The first device encountered with the IRQ bit set is
serviced and the subroutine is invoked.
• Easy to implement, but too much time spent on
checking the IRQ bits of all devices, though some
devices may not be requesting service.

## Slide 19: Vectored Interrupts (contd..)
The device requesting an interrupt may identify itself directly to the processor.
  Device can do so by sending a special code (4 to 8 bits) the processor over the bus.
  Code supplied by the device may represent a part of the starting address of the interrupt-service routine.
  The remainder of the starting address is obtained by the processor based on other information such as the range of memory addresses where interrupt service routines are located.
Usually the location pointed to by the interrupting device is used to store the starting address of the interrupt-service routine.
The processor reads this address called interrupt vector and loads into the PC, so it branches to that ISR
Notes: Repeat polling.
An alternative approach may be for the device which is requesting an interrupt to identify itself to the processor. This will avoid the overhead incurred by the polling itself.
The device may identify itself to the processor by sending a special code to the processor over the bus. This special code may be 4 to 8 bits. This special code used by the device to identify itself to the processor may also represent a part of the starting address of the ISR.
The remainder of the starting address could be obtained in a variety of ways such as the ISRs may reside in a particular section of the memory and hence may use memory addresses in a given range.
The code supplied by the device plus other information provides the starting address of the ISR. This starting address actually provides the actual starting address of the ISR.

## Slide 20: Interrupt Nesting
Previously, before the processor started executing the interrupt service routine for a device, it disabled the interrupts from the device.
In general, same arrangement is used when multiple devices can send interrupt requests to the processor.
  During the execution of an interrupt service routine of device, the processor does not accept interrupt requests from any other device.
  Since the interrupt service routines are usually short, the delay that this causes is generally acceptable.
However, for certain devices this delay may not be acceptable.
  Which devices can be allowed to interrupt a processor when it is executing an interrupt service routine of another device?
Notes: Repeat, that the processor did not want to be interrupted by the same device while it was executing its ISR, it disabled the interrupt at the beginning of the ISR, and it then enabled the interrupts before returning from the ISR.
In case of multiple devices, the same arrangement is used. That is, when the processor is executing the ISR of one device, it disables the interrupts not only from that device but also from all the other devices. That is, it does not accept interrupt requests from any other device.
Since ISRs are usually short, it takes very little time for their execution, as a result, the delay caused by not accepting interrupts from other devices while servicing an ISR is usually acceptable.
However, for some time critical devices this delay that may be caused may be unacceptable. So, that leads us to the question of which devices can interrupt a processor when it is executing an ISR of another device?

## Slide 21: Interrupt Nesting
I/O devices are organized in a priority structure:
  An interrupt request from a high-priority device is accepted while the processor is executing the interrupt service routine of a low priority device.
Pre-Emption of low priority Interrupt by another high
priority interrupt is known as Interrupt nesting
A priority level is assigned to a processor that can be changed under program control.
  Priority level of a processor is the priority of the program that is currently being executed.
  When the processor starts executing the interrupt service routine of a device, its priority is raised to that of the device.
  If the device sending an interrupt request has a higher priority than the processor, the processor accepts the interrupt request.
Notes: Repeat that multiple I/O devices may be connected to the processor. These multiple I/O devices may be organized according a certain priority. When the processor is servicing an interrupt from a device, only devices which have higher priority can interrupt the processor. That is, only devices which have higher priority can interrupt the processing of the ISR of the device of lower priority.
In order to implement this scheme, a priority level is assigned to a processor. This priority level can be changed under program control or it depends on which program is currently being executed by the processor. That is, the priority of the processor is the priority of the program that the processor is currently executing. When the processor receives an interrupt request from a device, and starts executing the ISR of that device, its priority is raised to that of the device. Now, if another device wants to interrupt the processor, then it is allowed to do so, only if its priority is higher than the priority of the processor which is set to the priority of the ISR of the device.

## Slide 22: Interrupts nesting
Processor’s priority is encoded in a few bits of the processor status register.
  Priority can be changed by instructions that write into the processor status register.
  Usually, these are privileged instructions, or instructions that can be executed only in the supervisor mode.
  Privileged instructions cannot be executed in the user mode.
  Prevents a user program from accidentally or intentionally changing the priority of the processor.
If there is an attempt to execute a privileged instruction in the user mode, it causes a special type of interrupt called as privilege exception.

## Slide 23: Interrupts
Priority arbitration
Device 1
Device 2
Device
p
Processor
INTA1
I
N
T
R
1
I
N
T
R
p
INTA
p
Each device has a separate interrupt-request and interrupt-acknowledge line.
Each interrupt-request line is assigned a different priority level.
Interrupt requests received over these lines are sent to a priority arbitration circuit
in the processor.
If the interrupt request has a higher priority level than the priority of the processor,
then the request is accepted.

## Slide 24: Simultaneous Request: DAISY CHAINING
Which interrupt request does the processor accept if it receives interrupt requests from two or more devices simultaneously?.
If the I/O devices are organized in a priority structure, the processor accepts the interrupt request from a device with higher priority.
  Each device has its own interrupt request and interrupt acknowledge line.
  A different priority level is assigned to the interrupt request line of each device.
However, if the devices share an interrupt request line, then how does the processor decide which interrupt request to accept?

## Slide 25: Interrupts (contd..)
Processor
Device 2
I
N
T
R
INTA
Device
n
Device 1
Polling scheme:
If the processor uses a polling mechanism to poll the status registers of I/O devices
to determine which device is requesting an interrupt.
In this case the priority is determined by the order in which the devices are polled.
The first device with status bit set to 1 is the device whose interrupt request is
accepted.
Daisy chain scheme:
Devices are connected to form a daisy chain.
Devices share the interrupt-request line, and interrupt-acknowledge line is connected
to form a daisy chain.
When devices raise an interrupt request, the interrupt-request line is activated.
The processor in response activates interrupt-acknowledge.
Received by device 1, if device 1 does not need service, it passes the signal to device 2.
Device that is electrically closest to the processor has the highest priority.

## Slide 26: Interrupts (contd..)
When I/O devices were organized into a priority structure, each device had its own
interrupt-request and interrupt-acknowledge line.
When I/O devices were organized in a daisy chain fashion, the devices shared an
interrupt-request line, and the interrupt-acknowledge propagated through the devices.
A combination of priority structure and daisy chain scheme can also used.
Device
Device
circuit
Priority arbitration
Processor
Device
Device
I
N
T
R
1
I
N
T
R
p
INTA1
INTA
p
Devices are organized into groups.
Each group is assigned a different priority level.
All the devices within a single group share an interrupt-request line, and are
connected to form a daisy chain.

## Slide 27: Controlling Device Request
Only those devices that are being used in a program should be allowed to generate interrupt requests.
To control which devices are allowed to generate interrupt requests, the interface circuit of each I/O device has an interrupt-enable bit.
  If the interrupt-enable bit in the device interface is set to 1, then the device is allowed to generate an interrupt-request.
Interrupt-enable bit in the device’s interface circuit determines whether the device is allowed to generate an interrupt request.
Interrupt-enable bit in the processor status register or the priority structure of the interrupts determines whether a given interrupt will be accepted.

## Slide 28: Direct Memory Access (contd..)
Direct Memory Access (DMA):
  A special control unit may be provided to transfer a block of data directly between an I/O device and the main memory, without continuous intervention by the processor.
Control unit which performs these transfers is a part of the I/O device’s interface circuit. This control unit is called as a DMA controller.
DMA controller performs functions that would be normally carried out by the processor:
  For each word transferred, it provides the memory address and all the control signals.
  To transfer a block of data, it increments the memory addresses and keeps track of the number of transfers.
Notes: This alternative approach is called as direct memory access. DMA consists of a special control unit which is provided to transfer a block of data directly between an I/O device and the main memory without continuous intervention by the processor.
A control unit which performs these transfers without the intervention of the processor is a part of the I/O device’s interface circuit, and this controller is called as the DMA controller.
DMA controller performs functions that would be normally be performed by the processor. The processor will have to provide a memory address and all the control signals. So, the DMA controller will also provide with the memory address where the data is going to be stored along with the necessary control signals. When a block of data needs to be transferred, the DMA controller will also have to increment the memory addresses and keep track of the number of words that have been transferred.

## Slide 29: Direct Memory Access (contd..)
DMA controller can transfer a block of data from an external device to the processor, without any intervention from the processor.
  However, the operation of the DMA controller must be under the control of a program executed by the processor. That is, the processor must initiate the DMA transfer.
To initiate the DMA transfer, the processor informs the DMA controller of:
  Starting address,
  Number of words in the block.
  Direction of transfer (I/O device to the memory, or memory to the I/O device).
Once the DMA controller completes the DMA transfer, it informs the processor by raising an interrupt signal.
Notes: Repeat DMA controller.
DMA controller can be used to transfer a block of data from an external device to the processor, without requiring any help from the processor. As a result the processor is free to execute other programs. However, the DMA controller should perform the task of transferring data to or from an I/O device for a program that is being executed by a processor. That is, the DMA controller does not and should not have the capability to determine when a data transfer operation should take place. The processor must initiate DMA transfer of data, when it is indicated or required by the program that is being executed by the processor.
When the processor determines that the program that is being executed requires a DMA transfer, it informs the DMA controller which sits in the interface circuit of the device of three things, namely, the starting address of the memory location, the number of words that needs to be transferred, and the direction of transfer that is, whether the data needs to be transferred from the I/O device to the memory or from the memory to the I/O device.
After initiating the DMA transfer, the processor suspends the program that initiated the transfer, and continues with the execution of some other program. The program whose execution is suspended is said to be in the blocked state.

## Slide 30: Direct Memory Access (contd..)
While a DMA Transfer is taking place, the program that requested the transfer cannot continue, and the processor can be used to execute another program.
After the DMA transfer is completed ,the processor can return to the program that requested the transfer.
The 0S is also responsible for suspending the execution of one program and starting another.
Thus for an I/O operation involving DMA, the OS puts the programs requested the transfer in BLOCKED STATE, initates the DMA transfer and starts execution of another program.
When transfer is completed, DMA controller informs the processor by sending interrupt request and os puts the suspended program to RUNNABLE STATE
Notes: Repeat DMA controller.
DMA controller can be used to transfer a block of data from an external device to the processor, without requiring any help from the processor. As a result the processor is free to execute other programs. However, the DMA controller should perform the task of transferring data to or from an I/O device for a program that is being executed by a processor. That is, the DMA controller does not and should not have the capability to determine when a data transfer operation should take place. The processor must initiate DMA transfer of data, when it is indicated or required by the program that is being executed by the processor.
When the processor determines that the program that is being executed requires a DMA transfer, it informs the DMA controller which sits in the interface circuit of the device of three things, namely, the starting address of the memory location, the number of words that needs to be transferred, and the direction of transfer that is, whether the data needs to be transferred from the I/O device to the memory or from the memory to the I/O device.
After initiating the DMA transfer, the processor suspends the program that initiated the transfer, and continues with the execution of some other program. The program whose execution is suspended is said to be in the blocked state.

## Slide 31: DMA controller registers(Contd…)
To start a DMA Transfer of a block of data from main memory to one of disks, a program writes the address and word count information into the registers of corresponding channel of disk controller.
DMA controller provides the disk controller with information to identify the data for future retrieval.
DMA controller proceeds independently to implement the specified operation.
When the DMA Transfer is completed, it is recorded in the status and control register of the DMA Channel by setting the DONE bit
At the same time if the IE bit =1,the controller sends an interrupt request to the processor and sets IRQ=1.
Status register also holds the other information ,such as whether transfer took place correctly or with errors

## Slide 32: Direct Memory Access (contd..)
Processor and DMA controllers have to use the bus in an interwoven/blended fashion to access the memory.
  DMA devices are given higher priority than the processor to access the bus.
  Among different DMA devices, high priority is given to high-speed peripherals such as a disk or a graphics display device.
Processor originates most memory access cycles on the bus.
  DMA controller can be said to “steal” memory access cycles from the bus. This interweaving technique is called as “cycle stealing”.
An alternate approach is the provide a DMA controller an exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block or burst mode.
Notes: Processor also has to transfer data to and from the main memory. Also, the DMA controller is responsible for transferring data to and from the I/O device to the main memory. Both the processor and the DMA controller have to use the external bus to talk to the main memory. Usually, DMA controllers are given higher priority than the processor to access the bus. Now, we also need to decide the priority among different DMA devices that may need to use the bus. Among these different DMA devices, high priority is given to high speed peripherals such as a disk or a graphics display device.
Usually, the processor originates most cycles on the bus. The DMA controller can be said to steal memory access cycles on from the bus. Thus, the processor and the DMA controller use the bus in an interwoven fashion. This interweaving technique is called as cycle stealing.
An alternate approach would be to provide DMA controllers exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block mode or the burst mode of operation.

## Slide 33: Bus arbitration
Processor and DMA controllers both need to initiate data transfers on the bus and access main memory.
The device that is allowed to initiate transfers on the bus at any given time is called the bus master.
When the current bus master relinquishes its status as the bus master, another device can acquire this status.
  The process by which the next device to become the bus master is selected and bus mastership is transferred to it is called bus arbitration.
Centralized arbitration:
  A single bus arbiter performs the arbitration.
Distributed arbitration:
  All devices participate in the selection of the next bus master.
Notes: Processor and DMA controllers both need to initiate data transfers on the bus and access main memory. The process of using the bus to perform a data transfer operation is called as the initiation of a transfer operation. At any point in time only one device is allowed to initiate transfers on the bus. The device that is allowed to initiate transfers on the bus at any given time is called the bus master. When the current bus master releases control of the bus, another device can acquire the status of the bus master. How does one determine which is the next device which will acquire the status of the bus master. Note that there may be several DMA controllers plus the processor which requires access to the bus. The process by which the next device to become the bus master is selected and bus mastership is transferred to it is called bus arbitration. There are two types of bus arbitration processes. Centralized arbitration and distributed arbitration. In case of centralized arbitration, a single bus arbiter performs the arbitration. Whereas in case of distributed arbitration all devices which need to initiate data transfers on the bus participate or are involved in the selection of the next bus master.

## Slide 34: Centralized Bus Arbitration
Processor
DMA
controller
1
DMA
controller
2
BG1
BG2
B
R
B
B
S
Y

## Slide 35: Centralized Bus Arbitration(cont.,)
Bus arbiter may be the processor or a separate unit connected to the bus.
Normally, the processor is the bus master, unless it grants bus membership to one of the DMA controllers.
DMA controller requests the control of the bus by asserting the Bus Request (BR) line.
In response, the processor activates the Bus-Grant1 (BG1) line, indicating that the controller may use the bus when it is free.
BG1 signal is connected to all DMA controllers in a daisy chain fashion.
BBSY signal is 0, it indicates that the bus is busy. When BBSY becomes 1, the DMA controller which asserted BR can acquire control of the bus.

## Slide 36: Centralized arbitration (contd..)
B
B
S
Y
BG1
BG2
Bus
master
B
R
Processor
DMA controller 2
Processor
T
ime
DMA controller 2
asserts the BR signal.
Processor asserts
the BG1 signal
BG1 signal propagates
to DMA#2.
Processor relinquishes control
of the bus by setting BBSY to 1.

## Slide 37: Distributed arbitration
All devices waiting to use the bus share the responsibility of carrying out the arbitration process.
  Arbitration process does not depend on a central arbiter and hence distributed arbitration has higher reliability.
Each device is assigned a 4-bit ID number.
All the devices are connected using 5 lines, 4 arbitration lines to transmit the ID, and one line for the Start-Arbitration signal.
To request the bus a device:
  Asserts the Start-Arbitration signal.
  Places its 4-bit ID number on the arbitration lines.
The pattern that appears on the arbitration lines is the logical-OR of all the 4-bit device IDs placed on the arbitration lines.

## Slide 38: Distributed arbitration

## Slide 39: Distributed arbitration(Contd.,)
Arbitration process:
  Each device compares the pattern that appears on the arbitration lines to its own ID, starting with MSB.
  If it detects a difference, it transmits 0s on the arbitration lines for that and all lower bit positions.
  The pattern that appears on the arbitration lines is the logical-OR of all the 4-bit device IDs placed on the arbitration lines.

## Slide 40: Distributed arbitration (contd..)
Device A has the ID 5 and wants to request the bus:
- Transmits the pattern 0101 on the arbitration lines.
Device B has the ID 6 and wants to request the bus:
- Transmits the pattern 0110 on the arbitration lines.
Pattern that appears on the arbitration lines is the logical OR of the patterns:
- Pattern 0111 appears on the arbitration lines.
Arbitration process:
Each device compares the pattern that appears on the arbitration lines to its own
ID, starting with MSB.
If it detects a difference, it transmits 0s on the arbitration lines for that and all lower
bit positions.
Device A compares its ID 5 with a pattern 0101 to pattern 0111.
It detects a difference at bit position 0, as a result, it transmits a pattern 0100 on the
arbitration lines.
The pattern that appears on the arbitration lines is the logical-OR of 0100 and 0110,
which is 0110.
This pattern is the same as the device ID of B, and hence B has won the arbitration.